## Slide 1
ECE ???
<Team Name>
Object Detection
Project Background
Hardware
Servo Driver
ECE Capstone Open House 2024
ECE 554
School Seeker
Nathan Woolf
Harrison Doll
Sam Cooper
Jake Neau
Cullen Krasselt
Went from YOLO algorithm & Color tracking to singular pixel tracking
Went from differencing every other frame to every frame by shrinking buffers in half, losing half the pixels stored, to store every frame to compare.
The pixel readout from the camera to the VGA controller happens at the rising edge of PIXLCLK. To determine whether a complete frame has been shown, we need to detect the falling edge of FRAME_VALID, as shown in Figure 2. With this information, we decided on a simple frame differencing formula (Figure 3) for determining whether there was a moving object in the camera or not.
Figure 2
Figure 3
The basis of our object detection depends on reading input from the Terasic TRDB-D5M camera and manipulating the camera module into detecting objects. The camera is connected via GPIO on the FPGA and converts analog data to digital in the form of a Bayer pixel array. The array alternates in a pattern of G1RG1R and BG2BG2 as shown in Figure 1.
Figure 1
Blah blah blah talk about the frame storing/differencing diagram
In order to make this project possible, a handful of hardware and peripherals were required. All peripherals are interfaced through GPIO signal pins.
Logic Level Shifter:
In support of FPGA logic, we were required to implement an external digital circuit to step-up the PWM logic levels for the servos. Due to the physical limitation of the FPGA’s GPIO output maximum voltage-current rating being set to 3.3V/1.5A, we were not able to drive the servo motors to their demanded 5V.
Additionally, this project integrated an off-the-shelf pan-tilt servo mount composed of two SG90 servo motors. One motor is responsible for moving in the horizontal direction, while the other controls the vertical position. As shown in the picture to the right
Logic Level Shifter High Level Schematic
To control the servos, the team decided to assemble servo driver modules to make their control simplified regardless of how position was communicated from image processing. The image to the right briefly describes how a servo motors PMW signal should be structured to achieve the desired servo horn position. The bounds of this specification were the motivating factoid to our servo driver. The formula relating servo horn position to duty cycle can be seen here:
Furthermore, the driver modules are parametrized to enable “overclocking” of the PWM signal frequency. Since the duty cycle, or the high pulse, of the period is constant (i.e 1ms for 0 degrees and 2ms for 180 degrees) we can shorten the low pulse of the period. This low period is in place to allow the internal comparator of the servo to correct its position. However, within in our application, the servo is constantly receiving new positional commands and thus we can afford the sacrifice in accuracy of position in exchange for greater speeds. For reference, typical hobbyist servo motors operate at 50Hz (hence the 20ms period in the image above). In this application, we were able to push our servos closer to 100Hz with no apparent fallbacks on accuracy.
Duty Cycle = 1000 + ( (degree_val * 1000.00) / 180)
The resulting duty cycle has units of microseconds, this ultimately gives a greater degree of accuracy than if we used floating point or another means of data representation. Successful simulation waveforms can be seen below highlighting the duty cycles from the image above
One of the important hardware components of our project was aligning the camera and laser setup so they were relatively in the same spatial planes. Therefore, the team decided to 3D model a mount for both the camera and the pan-tilt servo apparatus. The model was 3D printed at the Makerspace.
The project also made use of an off the shelf laser module for assigning the directionality of the system. We decided this sufficiently emulated the targeting nature of the system without using a projectile.
The project required a translation from Cartesian coordinates on the camera to spherical coordinates to drive the servos. However, trigonometric functions are hardware intensive and require a series expansion to approximate their values, which is inefficient on an FPGA. To reduce resource usage and improve speed, we approximated the angles by treating the x and y coordinates independently. This simplification allowed us to apply the small angle approximation, where tan(θ) ≈ θ, effectively eliminating the need for any trigonometric operations. The evolution of these equations is shown to the right.
Instead of passing angles between modules, we sent the number of microseconds directly to the servo driver. This offered finer control, with a resolution of 0.18 degrees per microsecond, and avoided the complexity of handling fixed-point numbers across modules. Our decision was supported by a heatmap of target positions, which showed most activity near the center, validating the small angle and linear control assumptions.
Instead of passing angles between modules, we sent the number of microseconds directly to the servo driver. This offered finer control, with a resolution of 0.18 degrees per microsecond, and avoided the complexity of handling fixed-point numbers across modules. Our decision was supported by a heatmap of target positions, which showed most activity near the center, validating the small angle and linear control assumptions.
To validate this approach, we generated a heatmap that visualizes the error introduced by the approximation. The results show that the primary source of error occurs near the corners of the camera frame, while most target positions along the axes and near the center remain close to the true values. This confirmed that our method was both accurate enough for our application, and that the improvements in efficiency were worth the losses in accuracy.
To validate this approach, we generated a heatmap that visualizes the error introduced by the approximation. The results show that the primary source of error occurs only near the corners of the camera frame, while most target positions remain close to the center, where the approximation holds well. This confirmed that our method was both efficient and accurate enough for our application.
Translation Layer